STYLES AND CHARACTERISTICS OF THE PRODUCTS COVERED BY THE CERTIFCATE:

| Style | Product code | Resistance values | Rated power dissipation |
| --- | --- | --- | --- |
| DC / DE | RCMT 1 | 10 Ohms to 1 MOhms | 1/2 W |
| AE / AC | RCMT 02 | 10 Ohms to 332 KOhms | 1/8 W |
| BE /BC | RCMT 05 | 10 Ohms to 1 MOhms | 1/4 W |

Tolerance: ± 0,5 ou/or ± 1 %

Temperature coefficient:	± 25 10-6/°C (code E)

± 50 10-6/°C (code C)

Assessment level: E

Climatic category: 55/125/56

Other characteristics: see detail specification.